## Slide 1: Chemical Equilibrium with Applications for MATLAB Quick Start Guide
Sam Kobliska, ERC Inc.
Chip Kopicz, ERC Inc.
2/7/2017

## Slide 2: CEA for MATLAB
Discuss basic MATLAB syntax for use in CEAM
Provide input format for using CEAM
Show data extraction from CEAM
  Structure format
  Screen
  File
Questions and practical application

## Slide 3: Content
Contents
  CEA for MATLAB file CEA.p
  CEA for MATLAB help file CEA.m
  CEA for MATLAB thermodynamic library thermo_lib.mat
  This CEAM slide package.

## Slide 4: How does CEA for MATLAB Work?
CEAM balances mass and energy to solve the combustion process.
Mass (Continuity)
  Mass is balanced at the atomic level. The sum of the products of the molar values and their respective number of nuclei must remain constant.
  Moles are not necessarily conserved
  Molecules are not necessarily conserved
Energy
  Energy is conserved by either using the user defined thermodynamic state or the thermodynamic database defined state, i.e. default values.
Assumptions
  The flow, if applicable, is axis-symmetric and 1-D
  Perfect Nozzle
  Instantaneous chemical reaction rate

## Slide 5: Basic MATLAB Syntax
Strings
  Strings must be encased in single quotation marks such as ‘string’
  Strings will show on the screen in magenta, such as ‘equilibrium’
  MATLAB is by its nature case sensitive. CEAM was written to remove as much case sensitivity as possible
Comments
  The comment symbol in MATLAB is a percentage sign (%)
  Comments can be on the same line as a command, but anything after the percentage sign is a comment.
  Comments appear on the screen in green
  For example: X=5; %X is the number of inputs
Line Termination
  The command line should to be terminated with a semicolon (;)
  If a semicolon is not used, the line will print to the screen
Line Continuation
  Command lines can be continued onto the next line with using an ellipsis (…)

## Slide 6: Basic MATLAB Syntax - Continued
Numbers
  Numeric values can be entered three ways.
    A number: 5
    As defined variable name: X when X has been defined in a previous line of code.
    An array: 1:0.2:5 which is in the format of initial_value:increment:end_value
      The end value can be the final value in the array, but that is not always true
      The final value is the last incremental value that satisfies the requirement that the array values be equal to or within the bounds of the end value
      For example: 1:4:10 has a end value of 10, but a final value of 9. (1,5,9)
      For example: 10:-4:1 has a end value of 1, but a final value of 2. (10,6,2)
      If the end value is greater than the initial value, the increment must be positive.
      Similarly, is the end value is less than the initial value, the increment must be negative
      If the array only consists of 2 inputs, then MATLAB assumes an increment of 1. For example: 12:30 is the same as 12:1:30
      Variable names can be used in arrays as well.
      For a example: x=1; y=0.2; z=5; x:y:z is acceptable
    The results can be combined for chamber conditions, for example:
      X=2500;
      …’p,psia’,1000:100:2000,X,3000,…
      The numeric inputs do not have to be in any particular order

## Slide 7: Input Deck Format
The CEAM input was designed to be as close to the legacy FORTRAN input as possible.
Example of a legacy FORTRAN input deck
problem hp
equilibrium
o/f=2.34
case=fastrak(O2/RP-1)
p(psi)=633.
reactants
fuel = RP-1(L) C=1. H=1.9423, wt% 100. h,cal/mol -5430. t(k) 300.0
oxid = O2(L) O=2., wt% 100. h,cal/mol -3032. t(k) 94.44
output calories transport
end
Step 1 in CEAM Conversion
  Add output assignment, and function call. The added text is in red to show contrast.
Output=CEA(problem hp
equilibrium
o/f=2.34
case=fastrak(O2/RP-1)
p(psi)=633.
reactants...

## Slide 8: Input Deck Format
Step 2
  Add commas to separate variables and bring inputs to a line format from a paragraph format. Remove equal signs and replace with commas
Output=CEA(problem,hp,equilibrium,o/f,2.34,case,fastrak(O2/RP-1),p(psi),633.,
reactants,fuel,RP-1(L),C,1.,H,1.9423,wt%,100.,h,cal/mol,-5430.,t(k),300.0,
oxid,O2(L),O,2,wt%,100.,h,cal/mol,-3032.,t(k),94.44,output,calories, transport,end
Step 3
  Encase words in single quotes
Output=CEA(‘problem’,’hp’,’equilibrium’,’o/f’,2.34,’case’,’fastrak(O2/RP-1)’, ’p(psi)’,633.,‘reactants’,’fuel’,’RP-1(L)’,’C’,1.,’H’,1.9423,’wt%’,100., ’h,cal/mol’,-5430.,’t(k)’,300.0,‘oxid’,’O2(L)’,’O’,2,’wt%’,100., ’h,cal/mol’,-3032.,’t(k)’,94.44,’output’,’calories’,‘transport’,’end’
Step 4
  Close the input with a closed parenthesis and a semicolon. The added text is in red to show contrast.
    Output=CEA(‘problem’,’hp’,’equilibrium’,’o/f’,2.34,’case’,’fastrak(O2/RP-1)’, ’p(psi)’,633.,‘reactants’,’fuel’,’RP-1(L)’,’C’,1.,’H’,1.9423,’wt%’,100., ’h,cal/mol’,-5430.,’t(k)’,300.0,‘oxid’,’O2(L)’,’O’,2,’wt%’,100., ’h,cal/mol’,-3032.,’t(k)’,94.44,’output’,’calories’,‘transport’,’end’);
Step 5
  Execute the code

## Slide 9: CEAM General Inputs
CEAM is called in MATLAB with the following syntax:
  Output_Variable=CEA(User_Defined_inputs);
    Where Output_Variable is the user defined variable that will store the structure that CEAM outputs
    “CEA“ is case sensitive
    User_Defined_inputs is the compilation of all applicable datasets
    Mandatory
      Reactants
      Problem
      End
    Optional
      Output
      Insert
      Only
      Omit
Datasets can be entered in any order except for “end” which must be the last dataset
Data entries are comma separated

## Slide 10: Reactant and Problem Datasets
What are the reactant and problem datasets and what do they each contain?
  Reactant Dataset
    The reactant dataset contains properties that are specific to the respective reactant
    It may be helpful to think of the reactant dataset as “manifold”, “upstream”, or “grain” conditions.
  Problem Dataset
    The problem dataset contains properties that are bulk combustion properties and are not specific to any reactant
    The problem dataset includes chamber and nozzle declarations, if applicable
    It may be helpful to think of the problem dataset as “chamber” conditions

## Slide 11: Mandatory Datasets
Reactant
  The reactant dataset contains:
    Type of each reactant
    Name of each reactant
    Chemical formula of each reactant
    Type of amount of each reactant (mass or mole)
    Amount of each reactant with respect to type of reactant
    Specific information such as enthalpy, temperature, or density for each reactant (if applicable) for each reactant
  In the event of duplicate input between the problem dataset and the reactant dataset, the reactant dataset input will be used and the problem dataset input will be dismissed.
Problem
  Problem contains the type of problem, and the bulk property inputs. The bulk property inputs vary on the type of problem and will be addressed on a later slide.
End
  End marks the end of an input

## Slide 12: Reactant Dataset
The reactant dataset contains all inputs to an assigned case that are specific to a reactant
  NOTE: The “library” option is slow and limits the reactant input and is not recommended.
Keyword
  The keyword for the reactant dataset is ‘reac’. Any word in the CEAM input that starts with the keyword will be recognized as the start of the reactant dataset.
Mandatory Input
  Reactant type
    Every reactant must start with a reactant type.
    The type declaration start as new reactant and ends any previous reactant definition.
    Each reactant must be completely defined before the next reactant is declared
    The keyword is a string input
    There are three reactant types and two acceptable input formats.

## Slide 13: Reactant Dataset - Continued
Mandatory Input – Continued
  Reactant type
    Name
      The keyword for name is ‘na’. Name is used if some reactants may contain both fuel and oxidizer components. Name is not common in liquid propulsion systems, but is common in solid propulsion systems. If name is used for one reactant, it must be used for all reactants.
      A bulk mixture ratio is undefined when using the “name” nomenclature since fuel and oxidizer is not defined.
    Fuel and Oxidizer Input Format
      The keyword for fuel is ‘fu’, and the keyword for oxidizer is ‘ox’

## Slide 14: Reactant Dataset - Continued
Mandatory Input – Continued
  Reactant name
    The reactant name is a variable name or string input and is not case sensitive
    The reactant name must immediately follow the propellant type declaration
    If the library option is used, the reactant name must match the name in the library
  Chemical formula
    The chemical formula is mandatory unless the library option is used.
    The chemical formula is not case sensitive.
    The chemical formula alternates between a string input of the atomic symbol and the number of atoms corresponding to the respective symbol
    The order in which the chemical formula is entered is irrelevant. ‘H’,2,’O’,1 and ‘O’,1,’H’,2 are recognized as the same formula.
  Type and amount of each reactant
    There are two types of reactant amounts recognized by CEAM. The types cannot be mixed.
    Moles
      The keyword is ‘m’.
      The molar amount of the propellant must immediately follow the keyword.
      Using molar amounts completely defines the mass balance of the reactants and a mixture ratio input in the problem dataset is unnecessary

## Slide 15: Reactant Dataset - Continued
Mandatory Input – Continued
  Type and amount of each reactant
    Mass or Weight Fraction and Name Propellant Type
      The keyword is ‘w’.
      The amounts are specific to the propellant type and also the complete mixture.
      The amounts are normalized to the mixture. The amounts do not have to add up to any particular number. For example, if reactant A has a weight fraction of 87, and reactant B has a weight fraction of 50, then the weight fraction of reactant A is 87/(87+50). Similarly, reactant B has a fraction of 50/(87+50).
      The amount value must follow the amount type. Only a single value is allowed.
      A bulk mixture ratio cannot be defined in the problem dataset when using this option.

## Slide 16: Reactant Dataset - Continued
Mandatory Input – Continued
  Type and amount of each reactant
    Mass or Weight Fraction and Fuel and Oxidizer Propellant Type
      The keyword is ‘w’.
      The amounts are specific to the propellant type.
      The amounts are normalized to the propellant type. The amounts do not have to add up to any particular number. For example, if fuel A has a weight fraction of 87, and fuel B has a weight fraction of 50, then the weight fraction of fuel A is 87/(87+50). Similarly, fuel B has a fraction of 50/(87+50).
      The amount value must follow the amount type. Only a single value is allowed.
      Note that the above fraction defines only the fuel and not the oxidizer.
      A bulk mixture ratio must be defined in the problem dataset when using this option.

## Slide 17: Reactant Dataset - Continued
Optional Input
  Note that that title of “optional input” may not be accurate. A given problem will require additional input that may be entered in either the reactant dataset as a reactant specific property or possibly in the problem dataset as a bulk property. In the event that a property is defined in both the reactant and problem datasets, CEAM will dismiss the problem dataset inputs(s), and include the reactant dataset input(s).
  Units are entered after the keyword. The two must be separated by a delimiter such as colon, semicolon, space, comma
  Temperature
    Temperature is required for HP, UV, and Rocket problems
    The input temperature should correspond to a upstream or “manifold” temperature
    The keyword for temperature is not case sensitive and is exactly ‘t’
    The allowable temperature are as follows:
    The temperature value must follow the amount type. Only a single value is allowed.
Temperature | Keyword
Rankine | R, r
Fahrenheit | F, f
Kelvin | K, k
Celsius | C, c

## Slide 18: Reactant Dataset - Continued
Optional Input - Continued
  Enthalpy
    Enthalpy is required for HP, and Rocket problems
    Enthalpy in the reactant dataset corresponds to reactant enthalpy
    The keyword for enthalpy is not case sensitive and is ‘h’
    The units are flexible. Enthalpy is in units of energy per mass. The allowable units energy and mass are not case sensitive and are as follows:
    The units of energy and mass must be separated by a division sign (/)
    The value of enthalpy must immediately follow the enthalpy keyword.
    Only a single value is allowed per reactant.
    The value of enthalpy must be the total enthalpy
    For example: …’h,calories/mole’,-2152,… is an acceptable input
Energy | Keyword(s)
BTU | Btu
calorie | Cal, c
kilocalorie | Kc, kiloc
Joule | J
kilojoule | Kj,kiloj
Mass | Keyword(s)
Gram | g
Kilogram | Kilog, kg
Pound Mass | Lbm
Mole | mol

## Slide 19: Reactant Dataset - Continued
Optional Input – Continued
  Energy
    Energy is required for UV problems
    The keyword for enthalpy is not case sensitive and is exactly ‘u’
    The units are the same as the units for enthalpy.
    The value of energy must immediately follow the energy keyword. Only a single value is allowed per reactant
  Density
    Density is completely optional
    The keyword for density is not case sensitive and is exactly ‘rho’
    The units are flexible. Density is in units of mass per volume. The allowable units mass and volume are not case sensitive and are as follows:
    The units of mass and volume must be separated by a division sign (/)
    The value of density must immediately follow the density keyword. Only a single value is allowed per reactant.
Volume | Keyword(s)
Cubic centimeter | cc
Cubic meter | m^3
Cubic foot | ft^3
Mass | Keyword(s)
Gram | g
Kilogram | Kg
Pound Mass | Lbm

## Slide 20: Reactant Dataset - Continued
Examples
'reactants','fuel','H2(L)','H',2,'wt%',100,'h,BTU/lbm',-1920.7,'t,r’,30.31,...
'oxid','O2(L)','O',2,'wt%',100,'h,Btu/Lbm',-174.263,'t,r',162.324,
'reac','oxid','Air','N',1.5617,'O',0.41959,'AR',0.00937,'C',0.00032,...
'wtfrac',1,'h,J/mol',12077.218,'t,k',700,'fuel','C7H8(L)','C',7,'H',8,...
'h,J/mol',12180,'wtfrac',0.4,'t,k',298.15,'fuel','C8H18(L)','C',8,'H',18,...
'h,J/mol',-250260,'wtfrac',0.6,'t,k',298.15,
'reactants','fuel','H2(G)','H',2,'wt%',100,'h,cal/mol','t:k',298,...
'oxid','O2(G)','O',2,'wt%',100,'h,cal/mol','t:k',298,
'reac','fuel','H2','H',2,'moles',1,'oxid','Air','N',1.5617,'O',0.41959,'AR',0.00937,'C',0.00032,'moles',1,
'reactants','name','HEHN','wt',44.500,'C',2,'H',9,'N',3,'O',4,'h,...
kcal/mol',-98.000,'rho,g/cc',1.428,'name','HAN','wt',41.830,'H',4,'N',2,...
'O',4,'h,kcal/mol',-95.300,'rho,g/cc',1.090,'name','AN','wt',02.225,'H',4,... 'N',2,'O',3,'h,kcal/mol',-87.380,'rho,g/cc',1.725, 'name','DIPY','wt',...
0.445,'C',10,'H',8,'N',2,'h,kcal/mol',44.478,'rho,g/cc',1.326,'name',...
'Water', 'wt',11.000,'H',2,'O',1,'h,kcal/mol',-68.313,'rho,g/cc',1.000,

## Slide 21: Problem Dataset
The problem dataset contains all the case type and all inputs to assigned case that are not specific to a reactant
‘prob’,’type’,’mixture type’,mixture value(s),’state variable 1’,state variable 1 value(s) ,’state variable 2’,state variable 2 value(s)…)
Mandatory
  Problem type
  State variables
  Mixture Ratio (if not moles in reactant dataset)
Optional
  Case title
Rocket
  Area ratio / Pressure ratio
  Equilibrium / Frozen
  Finite area chamber

## Slide 22: Problem Dataset
Assigned Variables | Keywords
Temperature and Pressure | TP, PT
Enthalpy and Pressure | HP, PH
Entropy and Pressure | SP, PS
Temperature and Volume(Density) | TV, VT
Energy and Volume(Density) | UV, VU
Entropy and Volume(Density) | SV, VS
Rocket | RKT, or RO
Shock | SH
Chapman-Jouget Detonation | DET
Mandatory Inputs
  Keyword
    The keyword is ‘prob'. The keyword is not case sensitive, and must be the first word in the dataset.
  Problem Type
    The problem type identifies the state variables that will be used to solve the combustion problem
    The problem type can be entered anywhere in the problem dataset
    State variable problem types are reversible. For example: ‘HP’, and ‘PH’ represent the same problem type
    The keywords for shock, detonation, and rocket are order sensitive. For example: ‘DET’ is recognized, but ‘TED’ is not recognized
    The problem type is not case sensitive

## Slide 23: Problem Dataset
Mandatory Inputs-Continued
  Problem Type Inputs
    Pressure
      Pressure is a required input for HP, TP, SP, Rocket, Shock, and Detonation problems
      Pressure will always be entered in the problem dataset
      The keyword for pressure is exactly ‘p‘ and it is not case sensitive
      The units are declared following the keyword and a delimiter
      The allowable units are not case sensitive and are as follows:
      The value(s) of pressure can be input as arrays, variables, and numerical values
Pressure | Keyword
Bar | bar
Atmosphere | atm
Pounds per square inch absolute | psi
Millimeters of mercury | mmh

## Slide 24: Problem Dataset
Mandatory Inputs-Continued
  Problem Type Inputs
    Temperature
      Temperature is a required input for TP, TV, and Detonation problems
      Temperature is optional for Rocket problems (can be helpful for low mixture ratio combustors)
      Temperature will always be entered in the problem dataset
      The keyword for temperature is exactly ‘t‘ and it is not case sensitive
      The units are declared following the keyword and a comma
      The allowable units are not case sensitive and are as follows:
      The value(s) of temperature can be input as arrays, variables, and numerical values
Temperature | Keyword
Kelvin | K
Celsius | C
Rankine | R
Fahrenheit | F

## Slide 25: Problem Dataset
Mandatory Inputs-Continued
  Problem Type Inputs
    Enthalpy
      Enthalpy is a required input for HP, and Rocket problems
      Enthalpy can be entered in either the problem dataset, or the reactant dataset. If enthalpy is entered both the problem dataset and the reactant dataset, the reactant dataset enthalpy will be used, and the problem dataset enthalpy input will be dismissed. If enthalpy is entered into the problem dataset, it must be the enthalpy of the product mixture.
      The keyword for enthalpy is exactly ‘h‘ and it is not case sensitive
      The units are flexible. Enthalpy is in units of energy per mass. The allowable units energy and mass are not case sensitive and are as follows:
      The units of enthalpy and mass must be separated by a division sign (/)
      The value of enthalpy must immediately follow the enthalpy keyword.
      The value of enthalpy must be the total enthalpy
      For example: …’h,calories/mole’,-2152,… is an acceptable input
      An alternative is units of h/R (kg-mole-K/kg-mixture)
Mass | Keyword(s)
Gram | g
Kilogram | Kilog, kg
Pound Mass | Lbm
Energy | Keyword(s)
BTU | Btu
calorie | Cal, c
kilocalorie | Kc, kiloc
Joule | J
kilojoule | Kj,kiloj

## Slide 26: Problem Dataset
Mandatory Inputs-Continued
  Problem Type Inputs
    Energy
      Energy is a required input for UV problems
      Energy can be entered in either the problem dataset, or the reactant dataset. If energy is entered both the problem dataset and the reactant dataset, the reactant dataset energy will be used, and the problem dataset energy input will be dismissed. If energy is entered into the problem dataset, it must be the energy of the product mixture.
      The keyword for energy is exactly ‘u‘ and it is not case sensitive
      The units of energy are identical to the units of enthalpy

## Slide 27: Problem Dataset
Mandatory Inputs-Continued
  Problem Type Inputs
    Entropy
      Entropy is a required input for SP problems
      Entropy must be entered in the problem dataset
      The keyword for entropy is exactly ‘s‘ and it is not case sensitive
      The units of entropy are in energy per mass-temperature. The units of entropy are similar to the units of enthalpy and energy. A temperature is added to the denominator.
      The units of energy and mass must be separated by a division sign (/)
      The value of entropy must immediately follow the entropy keyword.
      For example: …’s,J/kg-K’,… is an acceptable input
      An alternative is units of s/R (kg-mole/kg-mixture)
Mass | Keyword(s)
Gram | g
Kilogram | Kilog, kg
Pound Mass | Lbm
Energy | Keyword(s)
BTU | Btu
calorie | Cal, c
kilocalorie | Kc, kiloc
Joule | J
kilojoule | Kj,kiloj
Temperature | Keyword
Kelvin | K
Celsius | C
Rankine | R
Fahrenheit | F

## Slide 28: Problem Dataset
Mandatory Inputs-Continued
  Problem Type Inputs
    Specific Volume – Density
      Specific Volume or density are required for TV, UV, and SV problems
      Specific Volume or density must be entered in the problem dataset
      The keyword for specific volume is exactly ‘v‘ and it is not case sensitive
      The keyword for density is exactly ‘rho‘ and it is not case sensitive
      The units of specific volume are volume per mass
      The units of density are mass per volume
      The numerator and denominator must be separated by a division sign (/)
      The value(s) must immediately follow the keyword.
Mass | Keyword(s)
Gram | g
Kilogram | Kilog, kg
Pound Mass | Lbm
Volume | Keyword(s)
Cubic centimeter | cc
Cubic meter | m^3
Cubic foot | ft^3

## Slide 29: Problem Dataset
Mandatory Inputs-Continued
  Mixture Ratios
    Mixture ratio is required if the reactant amount defined in the reactant dataset are not in moles
    There are several keywords for the mixture ratio depending the definition of the mixture ratio. The mixture ratio types are as follows:
    More than one mixture ratio can be defined, but only one type of mixture ratio can be used for a single problem.
    The value(s) of mixture ratio can be input as arrays, variables, and numerical values
Optional – Case Name
  The case name is a file name printed in the output. The name is a string that follows the keyword ‘case‘.
  For example: ‘case’,’Example for class’,
Mixture Ratio Type | Keyword
Percent fuel by mass | %f
Fuel-to-oxidant weight ratio | f/o, f/a
Oxidant-to-fuel weight ratio | o/f
Equivalence Ratio (Equation 9.19 in NASA 1311) | phi
Chemical equivalence ratio (Equation 9.18 in NASA 1311) | r

## Slide 30: Problem Dataset
Rocket Problem
  Rocket problems are basically an HP problem or TP problem with additional inputs to address the nozzle, chamber, and flow type
    If temperature is not provided in the problem dataset, then the rocket problem will be treated as am HP problem. This is the typical approach.
    If temperature is provided in the problem dataset, then the rocket problem will be treated like a TP problem. This is not the typical approach, but it can be useful for low combustion temperature problems
  Basic assumptions
    Infinite Chamber
      CEAM assumes and infinite chamber (i.e. Mach=0). CEAM will assume isentropic flow through the throat and nozzle. A finite area chamber is available and will account for the losses associated with a non-zero Mach number. Input for a finite chamber will be described in a later section.
    No Nozzle
      CEAM assumes that there is no nozzle, but only a throat. The reason for this assumption is the throat can always be mathematically determined, but the nozzle must be defined by the user. Defining a nozzle will be described in a later section.
    Equilibrium
      CEAM assumes equilibrium flow. This means that the product composition is allowed to change such that the Gibbs free energy is minimized at every nozzle station. The flow can be defined as frozen flow which means the composition is not allow to change. The user can also decide at which station the flow is to be considered to be frozen. Defining frozen flow will be described in a later section.

## Slide 31: Problem Dataset
Rocket Problem
    Finite Chamber
      A finite chamber option is available to better estimate performance loss associated with chamber velocity.
      The finite chamber is always analyzed with equilibrium flow solutions in the subsonic flow areas
      The keyword for the finite chamber option is ’fac’ ,and is not case sensitive.
      Once the finite chamber option is declared, one type of finite chamber must be declared.
      Contraction Ratio
        Contraction ratio is one option of defining a finite area chamber
        The contraction ratio option assumes a cylindrical chamber
        The keyword for the contraction ratio option is ’ac’
        The value of the contraction ratio follows the acat declaration
        The value can be a single value or a variable
        The units of the contraction ratio are dimensionless
        For example: ’fac’,’acat’,2.5

## Slide 32: Problem Dataset
Rocket Problem
    Finite Chamber (continued)
      Mass Flux
        Mass flux ratio is the other option of defining a finite area chamber
        The keyword for the contraction ratio option is exactly ’ma’
        The provided mass flux is to be taken at the throat
        The value of the mass flux follows the ma units declaration
        The value can be a single value or a variable
        The mass flux units are mass per area-second
        The allowable units for mass and area are shown to the right
        The numerator and denominator must be separated by a division sign (/)
        For example: ’fac’,’ma,lbm/ft^2-s’,800
Mass | Keyword(s)
Gram | g
Kilogram | Kilog, kg
Pound Mass | Lbm
Area | Keyword
Square meter | m^2
Square millimeter | mm^2
Square inch | in^2
Square foot | ft^2

## Slide 33: Problem Dataset
Rocket Problem
    Chamber Stations
      CEAM allows nozzle and chamber stations to be defined two ways, Pressure ratio and area ratio
    Pressure Ratio
      Pressure ratios can used to define the nozzle
      Only a single solution exists for a defined pressure ratio. A supersonic or subsonic declaration is unnecessary
      Pressure ratios are dimensionless must be greater than 1
      The keyword is ’pi/p’
      The Pi pressure is the total pressure for an infinite chamber, and the chamber pressure for a finite chamber
      For example ’pi/p’,4,1.01,150,y

## Slide 34: Problem Dataset
Rocket Problem - Continued
  Chamber and Nozzle Definition
    Area Ratio
      Both a supersonic and subsonic solution exists for a given area ratio. Therefore, a keyword is used to define which solution the user wants
        Subsonic solutions use the keyword ’sub’
        Supersonic solutions use the keyword ’sup’
      Area ratios are dimensionless and be entered as numbers, arrays, and/or variables
      Area ratios must be greater than 1
      Subsonic area ratios must be less than the contraction ratio, if defined
      The area ratio values must follow the respective flow type
      The area ratios do not have to be entered in any particular order
      For example ’sub’,5,2,4,x,3:-0.1:1.5,’sup’,2,4,100,x,5
      In the output, subsonic area ratios are identified as a negative value
        An output title column of AR=5 refers to the supersonic solution whereas AR=-5 refers to the subsonic solution

## Slide 35: Problem Dataset
Rocket Problem - Continued
  Equilibrium and Frozen Flow
    Equilibrium
      Equilibrium is the default chemical flow type
      The composition is allowed to change to satisfy the minimization of the Gibbs free energy at each station
      The keyword for equilibrium flow is ’eq’, but it is unnecessary
    Frozen Flow
      Frozen flow is useful when chemical reaction time exceed nozzle residence time. That is, frozen flow is useful when the products will be ejected from the nozzle before the chemical reaction to reduce the Gibbs free energy can take place.
      The infinite chamber is always calculated as a equilibrium flow
      The user can control at what station the flow is frozen as an optional input
      CEAM will calculate equilibrium conditions to the point, and frozen conditions thereafter
      The keywords for frozen flow are ’fr’ and ’fz’
      The keywords for the frozen station is ’nfr’ and ’nfz’
      To freeze the flow at the throat, value is set equal to 2
      The value of nfz corresponds the supersonic column at which the flow should be declared to be frozen – refer to NASA RP-1311 Part II

## Slide 36: Problem Dataset - Continued
Examples
'problem','hp','o/f',6.0338,'case','Block_II_testing','p,psia',3126.24,
'prob','case','Example-3','hp','p(bar)',100,10,0.1,'o/f',17,
'problem','tp','eql','o/f',6.0:.2:7.0,'case','aerojet-gh2-go2(1000)', 'p,psi',1000.,2000,'t,R',5500:500:6500,
problem','case','Example-1','tp','p(atm)',1,0.1,0.01,'t(k)',3000,2000, 'r.eq.ratio',1,1.5,
'problem','sp','case','NameSP','o/f',6.00,'p,psi',628.960,'s/r',2.17959,
'problem','rocket','equilibrium','fac','acat',3,'o/f',2.34,2.5,'case','fastrak(O2/RP-1)','p(psi)',633,800,'subsonic(ae/at)',2.59,1.01, 'supsonic(ae/at)',1.01,15.0,30.0,
'problem','rocket','frozen','p,psia',300,'sup,ae/at',10.0000,
'problem','rocket','equilibrium','o/f',5.55157,'case','Example-8', 'p,bar',53.3172,'subar',1.58,'pi/p',10,100,1000,'supar',25,50,75,
'problem','rocket','equilibrium','o/f',5.55157,'case','Example-10','p,bar',53.3172,'fac','ma,kg/m^2',1333.9,'pi/p',10,100,1000,'supar',25:25:75,
'problem','rocket','equilibrium','case','Example-12','p,psi',1000,'pi/p', 68.0457,'o/f',2.5,'eql','fr','nfz',2,'sup',5,10,25,50,75,100,150,200,
'prob','hp','p,psia',1000,
'problem','rocket','fz','p,psia',300,'sup,ae/at',10.0000,
'problem','case','Example-2','phi,eq.ratio',1,'tv','t(k)',3000, 'rho,g/cc',9.186e-5,8.0877e-6,6.6054e-7

## Slide 37: Output Dataset
The output dataset contains keywords to identify the format of CEAMs output.
The output dataset is optional
    The output dataset keyword is ‘outp'
CEAM will always display/produce bulk thermodynamic properties and molar product composition fractions
Product Composition
  The product composition is a standard output of CEAM. The composition can be defined one of two ways
  Molar Fractions
    Molar fractions are the default definition of the product composition
    There is not a keyword for molar values
  Mass Fractions
    Mass fractions can be calculated as an output as an alternative to molar fractions
    The keyword for mass fractions is exactly ‘massf'

## Slide 38: Output Dataset
Units systems
  The default units of CEAM output are identical to the default units of the FORTRAN version. (SI mks with a few exceptions)
  Unit systems available in the FORTRAN version (default and calories) have been expanded in CEAM cgs, mks, and English
  The keywords are not case sensitive. The unit systems are as follows:
 | English | MKS | CGS | Default | Calories
keyword | eng | mks | cgs | N/A | cal
Pressure | psia | bar | mmh | Bar | Atm
Temperature | R | K | K | K | K
Density | lbm/ft^3 | kg/m^3 | g/cc | kg/m^3 | g/cc
Enthalpy | BTU/lbm | kJ/kg | J/g | kJ/kg | Cal/g
Energy | BTU/lbm | kJ/kg | J/g | kJ/kg | Cal/g
Gibbs | BTU/lbm | kJ/kg | J/g | kJ/kg | Cal/g
Entropy | BTU/lbm-R | kJ/kg-K | J/g-K | kJ/kg-K | Cal/g-K
Cp | BTU/lbm-R | kJ/kg-K | J/g-K | kJ/kg-K | Cal/g-K
Velocity | Ft/s | m/s | cm/s | m/s | m/s
Viscosity | lbm/ft-s | uPa-s | uPa-s | Millipoise | Millipoise
Thermal Conductivity | BTU/hr-ft-R | W/m-K | W/cm-K | mW/cm-K | Mcal/cm-K-s

## Slide 39: Output Dataset
Short
  Short eliminates the intermediate calculations from printing to the screen or file. Short will speed up the program, but can make debugging more difficult. The keyword is not case sensitive and is ‘short‘.
Trace
  Trace can be used to tighten the convergence value requirement to enhance accuracy for trace product species. The keyword is not case sensitive and is ‘trac‘. The value of trace may be a number or a variable.
Transport Properties
  Transport properties can be calculated by using the transport module in CEAM. The module default is OFF, but it will execute if the keyword ‘tran‘ is in the output dataset.

## Slide 40: Output Dataset - Continued
Examples
'output','tran',
'output','trace',1e-15,'mks',
'outp','transport','trac',1e-9,'mks',
'output','calories',
'output','short',
'output','transport','mks',
'output','massf','transport‘,’eng’
'output','mks',
'outp','massf','transport','mks‘
'output','transport','calories‘

## Slide 41: End Dataset
The end dataset ends the command for CEA with the one exception of the print option.
The end dataset is mandatory
    The end dataset keyword is ‘end‘
    The print option is entered after the end dataset
    If a print option is not entered, then CEAM will run in the background and write the data to the data structure. This is useful in a test data reduction routine.
    If the print option uses the keyword ‘screen’ then CEAM will print the output to the screen and the data structure.
    If the print option uses any other word, then an output file of that name is generated in the user’s file path. This is similar to what of the CEA FORTRAN did.

## Slide 42: Accessing Outputs
Three methods for output of CEAM
  1) Screen print
    Add ‘screen’ as the last very last input (after ‘end’)
  2) File print
    Add any name other than ‘screen’ as the last very last input (after ‘end’), and MATLAB will save the output file to that name in the MATLAB folder
    The output will be identical to the screen print
  3) Structure Array
    CEAM will always generate a structure array in the output variable declared in the command line

## Slide 43: Accessing the Structure Outputs
The output structure includes between five and seven fields
The structure can be opened either by typing the name into the command line, or by double clicking on it in the workspace
The fields of greatest interest will likely be “output”, and if applicable, “transport” and/or “rocket”
Double clicking on a field name will open the structure of that field

## Slide 44: Accessing the Structure Outputs-Continued
Below is an example of gamma from a Rocket problem
Gamma can be found either by double clicking on the appropriate field or by entering “x.output.gamma” into the command line

## Slide 45: Accessing the Structure Outputs-Continued
The final array is #MRx#PCx#T array except for rocket which is a #MRx#PCx#Area Ratio array
Consider a hydrogen-oxygen engine with MRs from 4.8-6.0 in increments of 0.1 and Pcs from 2800-3500 in increments of 100 psia
  The table of gammas is shown highlighted below. The header rows have been added for clarity

## Slide 46: Accessing Output- Continued
Examples
P=CEA('problem','rkt','equilibrium','o/f',MR,'p,psi',mcc_pc,...
'fac','acat',MCC_CR,'subar',MCC_CR-.01,... 'reactants','fuel','H2(L)','H',2,'wt%',...
100,'t,r',fu_t,'h,btu/lbm',fu_h,'oxid','O2(L)','O',2,'wt%',100,'t,r',ox_t,...
'h,btu/lbm',ox_h,'output','short','eng','end');
g=P.output.eql.gamma(4); % gamma
t=P.output.eql.temperature(4); % temperature
mw=P.output.eql.mw(4); % molecular weight-combustion products
P=CEA('problem','tp','equilibrium','o/f',GG_MR,'p,psi',FTIp,...
't,R',FTIt,'reactants','fuel','H2(L)','H',2,'wt%',100.,'h,btu/lbm',...
GG_Hf,'oxid','O2(L)','O',2,'wt%',100.,'h,btu/lbm',GG_Ho,'output',...
'short','eng','end');
SummarySheet(i,FTI_Cp_cn)=P.output.cp;
SummarySheet(i,FTI_enthalpy_cn)=P.output.enthalpy;
SummarySheet(i,FTI_entropy_cn)=P.output.entropy;
SummarySheet(i,FTI_gamma_cn)=P.output.gamma;
SummarySheet(i,FTI_mw_cn)=P.output.wm;
SummarySheet(i,FTI_r_cn)=P.output.cp-P.output.cp/P.output.gamma;
sr_FTI(i)=P.output.entropy;

## Slide 47: Generic Problem construction

## Slide 48: HP Problems
Enthalpy-Pressure (HP) problems are for equilibrium calculations only
Out=CEA(‘prob’,’HP’,’o/f’,6.2,’p,psia’,2000,’reac’,’fu’,’H2(G)’,’H’,2,’h,btu/lbm’,-112.9,’t(r)’,200,…
‘ox’,’O2(L)’,’O’,2,’h,btu/lbm’,-50.4,’t(r)’,170,’end’);
HP problems require, at a minimum, that:
  1) HP be declared
  2) At least one chamber pressure defined in the problem dataset
  3) At least one mixture ratio type and value defined in the problem dataset or moles defined in the reactant dataset
  4) Enthalpy defined either as a bulk property in the problem dataset, or enthalpy defined for every reactant
  5) A temperature defined for every reactant
4
1
3
2
5
4
5

## Slide 49: TP Problems
Temperature-Pressure (TP) problems are for equilibrium calculations only
Out=CEA(‘prob’,’TP’,’o/f’,6.2,’p,psia’,2000,’T(R),6200, …
’reac’,’fu’,’H2’,’H’,2,‘ox’,’O2(L)’,’O’,2,’end’);
TP problems require, at a minimum, that:
  1) TP be declared
  2) At least one chamber pressure defined in the problem dataset
  3) At least one mixture ratio type and value defined in the problem dataset or moles defined in the reactant dataset
  4) At least one combustion temperature defined
1
3
2
4

## Slide 50: SP Problems
Entropy-Pressure (SP) problems are for equilibrium calculations only
Out=CEA(‘prob’,’SP’,’o/f’,6.2,’p,psia’,2000,’S(btu/lbm-R),2.851,…
’reac’,’fu’,’H2’,’H’,2,‘ox’,’O2(L)’,’O’,2,’end’);
SP problems require, at a minimum, that:
  1) SP be declared
  2) At least one chamber pressure defined in the problem dataset
  3) At least one mixture ratio type and value defined in the problem dataset or moles defined in the reactant dataset
  4) At least one combustion entropy defined
1
3
2
4

## Slide 51: TV Problems
Temperature-Volume (TV) problems are for equilibrium calculations only
Out=CEA(‘prob’,’TV’,’o/f’,6.2,’rho,lbm/ft3’,1.1,’T(R),6200,’…
reac’,’fu’,’H2’,’H’,2,‘ox’,’O2(L)’,’O’,2,’end’);
TV problems require, at a minimum, that:
  1) TV be declared
  2) At least one combustion specific volume or density defined
  3) At least one mixture ratio type and value defined in the problem dataset or moles defined in the reactant dataset
  4) At least one chamber temperature defined in the problem dataset
1
3
2
4

## Slide 52: UV Problems
Energy-Volume (TV) problems are for equilibrium calculations only
Out=CEA(‘prob’,’UV’,’o/f’,6.2,’rho,lbm/ft3’,1.1,’u(btu/lbm), …
-2000,’reac’,’fu’,’H2’,’H’,2,‘ox’,’O2(L)’,’O’,2,’end’);
UV problems require, at a minimum, that:
  1) UV be declared
  2) At least one combustion specific volume or density defined
  3) At least one mixture ratio type and value defined in the problem dataset or moles defined in the reactant dataset
  4) At least one chamber energy defined in the problem dataset
1
3
2
4

## Slide 53: Rocket Problems
Rocket (rocket, rkt) problems are for both equilibrium and frozen calculations
Rocket problems are HP problems with more inputs
Out=CEA(‘prob’,’rocket’,’equilibrium’,’o/f’,6.2,’p,psia’,2000, …
’reac’,’fu’,’H2’,’H’,2,’h,btu/lbm’,-112.9,’t(r)’,200,‘ox’,’O2’,’O’,2,’h,btu/lbm’,50.4,’t(r)’,170,’end’);
Rocket problems require, at a minimum all HP property inputs and, that:
  1) Rocket be declared
  2) Equilibrium and/or frozen be declared
1
2